CSc72010

Shortest Paths and RIP

# Shortest Paths

Assume now that we have directed weighted links.  Each node knows the weights of all incident edges and the number of nodes in the graph.

Motivation is min-cost communication

Problem: Determine the shortest path from i0 to each other node.

This algorithm is the basis of Bellman-Ford, aka RIP (Route Information Protocol).  In the presence of failures this is an unstable routing protocol and isn’t much used.

We use a tree again: every node should output:

- its parent in the tree

- its distance from i0 in the (spanning) tree (sum of weights on edges)

We assume each node knows the weights of all incident edges and the number of nodes in the digraph.

## Bellman-Ford

Each node keeps track of the shortest known distance from i0 and updates it as new information arrives; also communicates changed distances.

statesi

dist:Int := infinity for i0 ~= i, 0 for i0

parent:Int := undefined

messagesi

send disti to all out-nbrs

transitionsi

[Relaxation step]:  if distj + weightji < disti for some in-nbr j of I, then update disti to distj + weightji and update parent to j

Terminates after n-1 rounds

Key Invariant Assertion:

At round r, 0 <= r <= n-1, every process i has its distance and parent components set to the shortest path values among those paths consisting of at most r edges.

Proof by Induction: Intuition – after r0-1 rounds, nodes at distance r0-1 have their best distances taken over all paths of <= r0-1 length.  At round r0, the nodes at distance r0 use these paths to compute their own shortest distances.

Complexity:

Time = n-1 (because shortest path can be over path with more links than diam)

Messages: (n-1)*|E|

Let’s suppose all nodes run this concurrently.  The result of the above algorithm is that destination nodes know the shortest path from each possible source.  To use this for routing, in practice, all the source nodes need to know the shortest distances and the next node on the path to each destination.    In fact, for routing, source nodes build a table like:

| Destination | Next hop | Distance (to destination) | Go through |
| --- | --- | --- | --- |

THis is non-trivial in a directed graph.  The importance of this, these days, is that under certain circumstances wireless networks may have some unidirectional links.  This table should be initialized with all destinations, with go through=destination, and distance=infinity.

Just the idea:

Then, all nodes could broadcast their own information in a message containing quadruples <src, dst, parent, distance>.  When a message arrives at the node X, for each quadruple <X, A, B, n> in the message, update the distance for destination A to be equal to n and if the entry in the “go through” column is A, then change it to B.  If the entry is not A, and the distance is less than the distance, save the quadruple.  The go through column works backwards along the path, until it gets back to an out-nbr of X.  Each time you update the go through column, check the set of saved tuples for one with A equal to the value in the go through column; if found, change the go through column to B and discard the tuple.

## RIP

This is the Internet algorithm that is based on the above shortest paths algorithm.

As usual, in practice, we assume a bidirectional network and therefore an undirected graph.  here’s how the algorithm works:

Assume:

Each node knows the “distance” to each directly-connected neighbor router – a link that is not there or down gets infinite cost.

Routing table:

A table Ri of distances to routers, initially only to directly-linked neighbors.

Initially, periodically, and whenever there is a change to the routing table Ri, send routing table to all neighboring routers.

On receiving a routing vector Rj from neighbor j, update your own routing table Ri using the rule:

If di(j) + Rj(k).distance < Ri(k).distance then

change Ri(k).to di(j) + Rj(k).distance

change next-hop (parent) to j

Example from Peterson & Davies, Figure 4.15, Table 4.5

|  | A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 0 | <1,B> | <1,C> |  | <1,E> | <1,F> |  |
| B | <1,A> | 0 | <1,C> |  |  |  |  |
| C | <1,A> | <1,B > | 0 | <1,D> |  |  |  |
| D |  |  | <1,C> | 0 |  |  | <1,G> |
| E | <1,A> |  |  |  | 0 |  |  |
| F | <1,A> |  |  |  |  | 0 | <1,G> |
| G |  |  |  | <1,D> |  | <1,F> | 0 |

Round 1.  A sends routing table to B, C, E, F; B sends routing table to A, C; C sends routing table to A, B; D sends routing table to C, G; E sends routing table to A; F sends routing table to A, G; G sends routing table to D, F.

|  | A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 0 | <1,B> | <1,C> | <2,C.> | <1,E> | <1,F> | <2,F> |
| B | <1,A> | 0 | <1,C> | <2,D> | <2,A> | <2,C> |  |
| C | <1,A> | <1,B > | 0 | <1,D> | <2,A> | <2,A> | <2,D> |
| D | <2,C> | <2,C> | <1,C> | 0 |  | <2,G> | <1,G> |
| E | <1,A> | <2,A> | <2,A> |  | 0 | <2,A> |  |
| F | <1,A> | <2,A> | <2,A> | <2,G> | <2,A> | 0 | <1,G> |
| G | <2,F> |  | <2,D> | <1,D> |  | <1,F> | 0 |

Round 2.

|  | A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 0 | <1,B> | <1,C> | <2,C.> | <1,E> | <1,F> | <2,F> |
| B | <1,A> | 0 | <1,C> | <2,D> | <2,A> | <2,C> | <3,A> |
| C | <1,A> | <1,B > | 0 | <1,D> | <2,A> | <2,A> | <2,D> |
| D | <2,C> | <2,C> | <1,C> | 0 | <3,C> | <2,G> | <1,G> |
| E | <1,A> | <2,A> | <2,A> | <3,A> | 0 | <2,A> | <3,A> |
| F | <1,A> | <2,A> | <2,A> | <2,G> | <2,A> | 0 | <1,G> |
| G | <2,F> | <3,F> | <2,D> | <1,D> | <3,F> | <1,F> | 0 |

Change weights, so that we don’t want to use the edge between F and G

|  | A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 0 | <1,B> | <1,C> |  | <1,E> | <1,F> |  |
| B | <1,A> | 0 | <1,C> |  |  |  |  |
| C | <1,A> | <1,B > | 0 | <1,D> |  |  |  |
| D |  |  | <1,C> | 0 |  |  | <1,G> |
| E | <1,A> |  |  |  | 0 |  |  |
| F | <1,A> |  |  |  |  | 0 | <12,G> |
| G |  |  |  | <1,D> |  | <12,F> | 0 |

Round 1.  A sends routing table to B, C, E, F; B sends routing table to A, C; C sends routing table to A, B; D sends routing table to C, G; E sends routing table to A; F sends routing table to A, G; G sends routing table to D, F.

|  | A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 0 | <1,B> | <1,C> | <2,C.> | <1,E> | <1,F> | <13,F> |
| B | <1,A> | 0 | <1,C> | <2,D> | <2,A> | <2,A> |  |
| C | <1,A> | <1,B > | 0 | <1,D> | <2,A> | <2,A> | <2,D> |
| D | <2,C> | <2,C> | <1,C> | 0 |  | <13,G> | <1,G> |
| E | <1,A> | <2,A> | <2,A> |  | 0 | <2,A> |  |
| F | <1,A> | <2,A> | <2,A> | <2,G> | <2,A> | 0 | <12,G> |
| G | <13,F> |  | <2,D> | <1,D> |  | <12,F> | 0 |

Round 2.

|  | A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 0 | <1,B> | <1,C> | <2,C.> | <1,E> | <1,F> | <3,C> |
| B | <1,A> | 0 | <1,C> | <2,D> | <2,A> | < 2,A> | <3,C> |
| C | <1,A> | <1,B > | 0 | <1,D> | <2,A> | <2,A> | <2,D> |
| D | <2,C> | <2,C> | <1,C> | 0 | <3,C> | <3,C> | <1,G> |
| E | <1,A> | <2,A> | <2,A> | <3,A> | 0 | <2,A> | <14,A> |
| F | <1,A> | <2,A> | <2,A> | <2,G> | <2,A> | 0 | <12,G> |
| G | <2,F> | <3,F> | <2,D> | <1,D> | <14,F> | <12,F> | 0 |

Round 3.

|  | A | B | C | D | E | F | G |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 0 | <1,B> | <1,C> | <2,C.> | <1,E> | <1,F> | <3,C> |
| B | <1,A> | 0 | <1,C> | <2,D> | <2,A> | < 2,A> | <3,C> |
| C | <1,A> | <1,B > | 0 | <1,D> | <2,A> | <2,A> | <2,D> |
| D | <2,C> | <2,C> | <1,C> | 0 | <3,C> | <3,A> | <1,G> |
| E | <1,A> | <2,A> | <2,A> | <3,A> | 0 | <2,A> | <4,A> |
| F | <1,A> | <2,A> | <2,A> | <2,G> | <2,A> | 0 | <4,A> |
| G | <2,F> | <3,F> | <2,D> | <1,D> | <3,F> | <4,D> | 0 |