Kernel Module Program Examples

- The following link is for kernel module programming guide and Linux filesystem hierarchy

http://tldp.org/LDP/lkmpg/2.6/html/index.html

http://tldp.org/LDP/Linux-Filesystem-Hierarchy/html/index.html

hello_module.c

#include <linux/kernel.h>

#include <linux/module.h>

int hello_module_init(void)

{

printk(KERN_EMERG "Hello Module~! I'm in Kernel\n");

return 0;

}

void hello_module_cleanup(void)

{

printk("<0>Bye Module~!\n");

}

module_init(hello_module_init);

module_exit(hello_module_cleanup);

MODULE_LICENSE("GPL");

Makefile

MY_TARGET	:= hello_module.ko

obj-m		:= hello_module.o

KERNEL_DIR	:= /lib/modules/$(shell uname -r)/build

MODULE_DIR	:= /lib/modules/$(shell uname -r)/kernel/hello_module

PWD		:= $(shell pwd)

default :

$(MAKE) -C $(KERNEL_DIR) SUBDIRS=$(PWD) modules

install :

mkdir -p $(MODULE_DIR)

cp -f $(MY_TARGET) $(MODULE_DIR)

clean :

$(MAKE) -C $(KERNEL_DIR) SUBDIRS=$(PWD) clean

Some commands need super user privilege

- You need to use kernel module make mechanism available in your /lib/modules/your_kernel_version/build directory.

- The hello_module.c uses module_init() macro and module_exit() macro to execute hello_module_init function by insmod command and hello_module_cleanup function by rmmod command.

- Steps to create hello_module.ko kernel module object

  - In the source directory $make

  - See files created by make

  - $insmod hello_module.ko //then you can see Hello Module~ I/m in Kernel message from syslogd

  - $rmmod hello_module //you will see Bye Module~!

  - make install will copy the module to MODULE_DIR

  - make clean will remove some generated files

Character device driver kernel module generation. Some commands need super user privilege.

- Create chr_driver/driver directory

chr_test.c

#include <linux/kernel.h>

#include <linux/module.h>

#include <linux/slab.h>

#include <linux/fs.h>

#include <asm/uaccess.h>

#define DEVICE_NAME 	"mydrv"

#define MYDRV_MAX_LENGTH	4096

#define MIN(a, b) (((a) < (b)) ? (a) : (b))

static int MYDRV_MAJOR;

static char * mydrv_data;

static int mydrv_read_offset, mydrv_write_offset;

static int mydrv_open(struct inode *inode, struct file *file)

{

if( MAJOR(inode->i_rdev) != MYDRV_MAJOR )

return -1;

return 0;

}

static int mydrv_release(struct inode * inode, struct file *file)

{

if( MAJOR(inode->i_rdev) != MYDRV_MAJOR )

return -1;

return 0;

}

static int mydrv_ioctl(struct inode *inode, struct file *file, unsigned int cmd, unsigned long arg)

{

printk("<0> mydrv_ioctl is invoked\n");

return 0;

}

static ssize_t mydrv_read(struct file *file, char *buf, size_t count, loff_t *ppos)

{

if( (buf == NULL) || (count < 0 ) )

return -EINVAL;

if( (mydrv_write_offset - mydrv_read_offset) <= 0 )

return 0;

count = MIN( (mydrv_write_offset - mydrv_read_offset), count );

if( copy_to_user(buf, mydrv_data + mydrv_read_offset, count) )

return -EFAULT;

mydrv_read_offset += count;

return count;

}

static ssize_t mydrv_write(struct file *file, const char *buf, size_t count, loff_t *ppos)

{

if( (buf==NULL) || (count<0) )

return -EINVAL;

if( count+mydrv_write_offset >= MYDRV_MAX_LENGTH) {

/* driver space is too small */

return 0;

}

if( copy_from_user(mydrv_data + mydrv_write_offset, buf, count) )

return -EFAULT;

mydrv_write_offset += count;

return count;

}

struct file_operations mydrv_fops = {

.owner = THIS_MODULE,

.read = mydrv_read,

.write = mydrv_write,

/*	.ioctl = mydrv_ioctl, */

.open = mydrv_open,

.release = mydrv_release,

};

int mydrv_init(void)

{

if( (MYDRV_MAJOR = register_chrdev(0, DEVICE_NAME, &mydrv_fops)) < 0 ){

printk("<0> can't be registered\n");

return MYDRV_MAJOR;

}

printk("<0> major NO = %d\n", MYDRV_MAJOR);

if( (mydrv_data = (char *) kmalloc(MYDRV_MAX_LENGTH * sizeof(char), GFP_KERNEL)) == NULL ){

unregister_chrdev(MYDRV_MAJOR, DEVICE_NAME);

return -ENOMEM;

}

mydrv_read_offset = mydrv_write_offset = 0;

return 0;

}

void mydrv_cleanup(void)

{

kfree(mydrv_data);

unregister_chrdev(MYDRV_MAJOR, DEVICE_NAME);

}

module_init(mydrv_init);

module_exit(mydrv_cleanup);

Makefile

MY_TARGET	:= chr_test.ko

obj-m		:= chr_test.o

KERNEL_DIR	:= /lib/modules/$(shell uname -r)/build

MODULE_DIR	:= /lib/modules/$(shell uname -r)/kernel/chr_test

PWD		:= $(shell pwd)

default :

$(MAKE) -C $(KERNEL_DIR) SUBDIRS=$(PWD) modules

install :

mkdir -p $(MODULE_DIR)

cp -f $(MY_TARGET) $(MODULE_DIR)

clean :

$(MAKE) -C $(KERNEL_DIR) SUBDIRS=$(PWD) clean

mydrv_test.c

#include <stdio.h>

#include <fcntl.h>

#define MAX_BUFFER	26

char buf_in[MAX_BUFFER];

char buf_out[MAX_BUFFER];

int main(void)

{

int fd, i, c = 65;

if( (fd = open("/dev/mydrv", O_RDWR)) < 0 ){

perror("open error");

return -1;

}

for(i = 0; i<MAX_BUFFER; i++){

buf_out[i] = c++;

buf_in[i] = 65;

}

for(i = 0; i<MAX_BUFFER; i++){

fprintf(stderr, "%c", buf_in[i]);

}

fprintf(stderr, "\n");

write(fd, buf_out, MAX_BUFFER);

for(i = 0; i<MAX_BUFFER; i++){

fprintf(stderr, "%c", buf_out[i]);

}

fprintf(stderr, "\n");

close(fd);

return 0;

}

- $make

- $insmod chr_test.ko

  - We have 0-255 major numbers and 0-255 minor numbers to identify a unique driver

- $mknod /dev/mydrv c 253 0 //create a special file to access character device driver module you created. $man mknod

- Move to the chr_driver/app directory $gcc –O –o mydrv_test mydrv_test.c //optimize the executable code

- $./mydrv_test //see whether you get the correct result AAAAAAAAAAA.. ABC….Z