## Slide 1: Lesson 1
Introduction: Computer
Abstractions and
Technology

## Slide 2: Classes of computing applications and their characteristics
Computers are used in three different classes of applications:
  Personal computers(PCs)
  Servers
  Embedded computers

## Slide 3: Personal Computers (PCs)
A computer designed for use by an individual, usually incorporating a graphics display, a keyboard, and a mouse.
For example, a home computer kept on a desktop and used by family members for emails, web browsing, social networking, movie watching, distance learning.

## Slide 4: Servers
A computer used for running larger programs for multiple users, often simultaneously, and typically accessed only via a network.
Example: A computer in an Amazon building accessed by thousands of people for online shopping.
Servers span the widest range in cost and capability.
At the low end, a server may be little more than a desktop computer without a screen or keyboard and cost a thousand dollars. Or can be supercomputers
Low end server can be used for file storage.

## Slide 5: Supercomputer:
A class of computers with the highest performance and cost; they are configured as servers and typically cost tens to hundreds of millions of dollars.
They are used for scientific and engineering research and applications
Supercomputers consist of tens of thousands of processors and many terabytes of memory

## Slide 6: Summit – IBM

## Slide 8: Embedded computer:
A computer inside another device used for running one predetermined application or collection of software
Examples of embedded computers include:
  Microprocessors found in your car
  Computers in a television set
  Networks of processors that control a modern airplane or cargo ship
  A computer in a cardiac pacemaker, which delivers electric shocks to keep a human's heart beating properly.

## Slide 9: PostPC era
Mobile phones Iphone, Androids
Personal mobile devices (PMDs) are small wireless devices to connect to the Internet; they rely on batteries for power, and software is installed by downloading apps. Conventional examples are smart phones and tablets.
PMDs rely on a touch-sensitive screen or even speech input

## Slide 10: Cloud Computing
Cloud computing refers to large collections of servers that provide services over the Internet; some providers rent dynamically varying numbers of servers as a utility.
Cloud Computing relies on giant datacenters called Warehouse Scale Computers (WSCs)
Software as a Service(SaaS) is deployed via cloud computing

## Slide 11: Software as a Service
(SaaS) delivers software and data as a service over the Internet, usually via a thin program such as a browser that runs on local client devices, instead of binary code that must be installed, and runs wholly on that device. Examples include web search and social networking.

## Slide 12: Eight Great Ideas in Computer Architecture
Design for Moore’s Law
Use Abstraction to Simplify Design
Make the Common Case Fast
Performance via Parallelism
Performance via Pipelining
Performance via Prediction
Hierarchy of Memories
Dependability via Redundancy

## Slide 13: Design for Moore’s Law
Moore’s Law states that integrated circuit(IC) resources double every 18–24 months.
Moore’s Law resulted from a 1965 prediction of such growth in IC capacity made by Gordon Moore, one of the founders of Intel.
Computer architects must anticipate where the technology will be when the design finishes rather than design for where it starts.

## Slide 14: Use Abstraction to Simplify Design
Major productivity technique for hardware and software is to use abstractions to represent the design at diff erent levels of representation; lower-level details are hidden to offer a simpler model at higher level

## Slide 15: Make the Common Case Fast
Making the common case fast will tend to enhance performance better than optimizing the rare case.

## Slide 16: Performance via Parallelism
Getting more performance by performing operations in parallel

## Slide 17: Performance via Pipelining
Pipelining, which moves multiple operations through hardware units that each do a piece of an operation, akin to water flowing through a pipeline.

## Slide 18: Performance via Prediction
The idea of prediction is that, in some cases it can be faster on average to guess and start working rather than wait until you know for sure, assuming that the mechanism to recover from a misprediction is not too expensive and your prediction is relatively accurate.

## Slide 19: Hierarchy of Memories
Programmers want memory to be fast, large, and cheap, as memory speed oft enshapes performance, capacity limits the size of problems that can be solved
Architects have found that they can address these conflicting demands with a hierarchy of memories, with the fastest, smallest, and most expensive memory per bit at the top of the hierarchy and the slowest, largest, and cheapest per bit at the bottom. As

## Slide 20: Dependability via Redundancy
Computer should be dependable.
We know the hardware can fail so to make a computer dependable you can include redundant components that can take over when a failure occurs and to help detect failures

## Slide 21: Computer System
The hardware in a computer can only execute extremely simple low-level instructions
To go from a complex application to the simple instructions involves several layers of software that interpret or translate high-level operations into simple computer instructions, an example of the great idea of abstraction.
Systems software: Software that provides services that are commonly useful, including operating systems, compilers, loaders, and assemblers.

## Slide 22: A simplified view of hardware and software as hierarchical layers, shown as concentric circles with hardware in the center and applications software outermost
Systems software sitting between the hardware and applications software.
There are many types of systems soft ware, but two types of systems software are central to every computer system today: an operating system and a compiler.
An operating system interfaces between a user’s program and the hardware and provides a variety of services and supervisory functions.
Compiler is a program that translates high-level language statements into assembly language statements.

## Slide 23: Hardware and Software
High-level programming language: A portable language such as C, C++, Java, or Visual Basic that is composed of words and algebraic notation that can be translated by a compiler into assembly language.
Assembler: A program that translates a symbolic version of instructions into the binary version.
Assembly language: A symbolic representation of machine instructions.
derstands is the machine language.
Assembler: A program that translates a symbolic version of instructions into the binary version.
Assembly language: A symbolic representation of machine instructions.

## Slide 24: The organization of a computer
A computer consists of the following five classic components
  Control
  Memory
  Input
  Output
  Data path
The datapath and control are collectively called processor

## Slide 25: Basic Functions of the Computer Hardware
Inputting data
Outputting data
Processing data
And storing data

## Slide 26: Input devices
Input devices are used to feed the computer information.
Examples of input devices include keyboard, mouse

## Slide 27: Output Devices
A mechanism that conveys the result of a computation to a user, such as a display, or to another computer.

## Slide 28: The five components of a computer

## Slide 29: The organization of a computer
At a basic level, a computer consists of three pieces
  A processor to interpret and execute programs
  A memory to store both data and programs
  A mechanism for transferring data to and from the outside world
The processor gets instructions and data from memory. Input writes data to memory, and output reads data from memory. Control sends the signals that determine the operations of the datapath, memory, input, and output.

## Slide 30: Organization of a computer
The processor gets instructions and data from memory. Input writes data to memory, and output reads data from memory. Control sends the signals that determine the operations of the datapath, memory, input, and output.

## Slide 31: Central processor unit (CPU)
The CPU is also called the processor
This is the active part of the computer, which contains the datapath and control and which adds numbers, tests numbers, signals I/O devices to activate, and so on.
The processor logically comprises two main components: datapath and control
The datapath performs the arithmetic operations.
Control tells the datapath, memory, and I/O devices what to do according to the wishes of the instructions of the program

## Slide 32: Memory
It is the storage area where programs are kept when they are running and it contains the data needed by the running programs.
The memory is built from DRAM chips,
DRAM stands for dynamic random access memory
DRAM is volatile as it only returns data only when it is receiving power
Inside the processor there is another type of memory—cache memory.

## Slide 33: Cache memory
Cache memory: A small, fast memory that acts as a buffer for a slower, larger memory.
Cache is built using a different memory technology, static random access memory (SRAM). SRAM is faster but less dense, and hence more expensive, than DRAM

## Slide 34: Instruction set architecture and Application binary interface (ABI):
Also called architecture.
An abstract interface between the hardware and the lowest-level software that encompasses all the information necessary to write a machine language program that will run correctly, including instructions, registers, memory access, I/O, and so on.
Application binary interface (ABI): The user portion of the instruction set plus the operating system interfaces used by application programmers. It defines a standard for binary portability across computers.

## Slide 35: Nonvolatile memory vs Volatile memory
Volatile memory is the storage, such as DRAM, that retains data only if it is receiving power. This is also called main memory or primary memory
Nonvolatile memory is a form of memory that retains data even in the absence of a power source and that is used to store programs between runs. A DVD disk is nonvolatile. This is called secondary memory

## Slide 36: Communicating with other computers
Networks interconnect whole computers, allowing computer users to extend the power of computing by including communication.
Networked computers have several major advantages:
  Communication: Information is exchanged between computers at high speeds.
  Resource sharing: Rather than each computer having its own I/O devices, computers on the network can share I/O devices.
  Nonlocal access: By connecting computers over long distances, users need not be near the computer they are using.

## Slide 37: Networks
Local area network (LAN): A network designed to carry data within a geographically confined area, typically within a single building.
Wide area network (WAN): A network extended over hundreds of kilometers that can span a continent.

## Slide 38: Reading
Hennessy and Patterson Chapter 1.1 through 1.4