## Slide 1: Lesson 2
Instructions: Language of the Computer

## Slide 2: Machine Language and Assembly Language
To command a computer’s hardware, you must speak its language.
The words of a computer’s language are called instructions, and its vocabulary is called an instruction set.
Computer instructions can be represented as sequences of bits. This representation is called machine language
A slightly higher-level representation (and one that is much easier for humans to use) is called assembly language
The chosen instruction set comes from MIPS Technologies.

## Slide 3: Three Other Popular Instruction Sets
ARMv7 is similar to MIPS.
Intel x86, which powers both the PC and the cloud of the PostPC Era
ARMv8, which extends the address size of the ARMv7 from 32 bits to 64 bits

## Slide 4: Stored-program Computer Concept
Stored-program computer is the idea that instructions and data of many types can be stored in memory as numbers

## Slide 5: Operations Of The Computer Hardware
Every computer must be able to perform arithmetic
Example of MIPS assembly language notation:
  add a, b, c
  The above means add b and c and put the result in a
In MIPS, data must be in registers to perform arithmetic

## Slide 6: Three Underlying Principles Of Hardware Design:
Simplicity favors regularity.
Smaller is faster

## Slide 7: MIPS Assembly Language
MIPS stands for Microprocessor without Interlocked Pipeline Stages
MIPS assembly language is a 3-address assembly language. Operands are either immediates or in registers.
There are 32 registers that we commonly use. Each is 32 bits wide. The registers are identified by an integer, numbered 0 - 31.
To reference a register as an operand, use the syntax $x, where x is the number of the register you want. examples: $12, $15

## Slide 8: The MIPS Assembly Language Notation
add a, b, c
The above MIPS assembly language notation instructs a computer to add the two variables b and c and to put their sum in a.
Type a MIPS add instruction that computes: z = x + y
Solution: add z, x, y or add z y, x
The natural number of operands for an operation like addition is three: the two numbers being added together and a place to put the sum.

## Slide 9: MIPS Notation
This notation is rigid in that each MIPS arithmetic instruction performs only one operation and must always have exactly three variables.

## Slide 10: Example of Compiling Two C Assignment Statements into MIPS.
C Code
  a = b + c;
  d = a - e;
MIPS
  add a, b, c # register a contains b + c
  sub d, a, e # register d contains a – e
Sharp symbol (#) on each line is a comment

## Slide 11: Basic instruction execution.
Given: b = 2, c = 5, d = 1.
add a, b, c. What is the final value of a?
add t, d, c
add a, t, c # What is the final value of a
sub t, c, b
add a, t, d # What is the final value of a

## Slide 12: Example 1 of compiling a complex C assignment into MIPS.
C Code
  f = (g + h) - (i + j);
MIPS
  add t0, g, h # temp t0 contains g + h
  add t1, i, j # temp t1 contains i + j
  sub f, t0, t1 # f gets t0 - t1, which is (g + h) - (i + j)

## Slide 13: Examples
add $s1, $s2, $s3
addi $s1, $s3, 50

## Slide 14: MIPS Continued
The natural number of operands for an operation like addition is three: the two numbers being added together and a place to put the sum.
Requiring every instruction to have exactly three operands, no more and no less, conforms to the philosophy of keeping the hardware simple: hardware for a variable number of operands is more complicated than hardware for a fixed number. This situation illustrates the first of three underlying principles of hardware design:

## Slide 15: MIPS operands

## Slide 16: Instruction Types
Data movement instructions:
  Data movement instructions are the most frequently used instructions. Data is moved from memory into registers, from registers to registers, and from registers to memory, and many machines provide different instructions depending on the source and destination.
Arithmetic instructions:
  Instructions that use integers and floating-point numbers.
  Many instruction sets provide different arithmetic instructions for various data sizes
  Arithmetic operations occur only on registers in MIPS instructions

## Slide 17: MIPS assembly language for Arithmetic

## Slide 18: MIPS assembly language Data Transfer

## Slide 19: Instruction Types Continued
Boolean logic instructions:
  Instructions perform Boolean operations, much in the same way that arithmetic operations work.
  Instructions for performing AND, NOT, and often OR and XOR operations.
Bit manipulation (shift and rotate)
  Bit manipulation instructions are used for setting and resetting individual bits (or sometimes groups of bits) within a given data word. These include both arithmetic and logical shift instructions and rotate instructions, both to the left and to the right. Logical shift instructions simply shift bits to either the left or the right by a specified amount, shifting in zeros from the opposite end.

## Slide 20: Instruction Types Continued
I/O instructions
  The basic schemes for handling I/O are programmed I/O, interrupt-driven I/O, and DMA devices
Transfer of control instructions
  Control instructions include branches, skips, and procedure calls. Branching can be unconditional or conditional. Skip instructions are basically branch instructions with implied addresses. Because no operand is required, skip instructions often use bits of the address field to specify different situations
Special purpose instructions
  Special purpose instructions include those used for string processing, high-level language support, protection, flag control, and cache management. Most architectures provide instructions for string processing, including string manipulation and searching.

## Slide 21: MIPS assembly language logical

## Slide 22: Assembly Language

## Slide 23: Operands of the Computer Hardware
The operands of arithmetic instructions are restricted; they must be from a limited number of special locations built directly in hardware called registers
The size of a register in the MIPS architecture is 32 bits; groups of 32 bits occur so frequently that they are given the name word in the MIPS architecture
In the MIPS architecture, each register is 32 bits wide.

## Slide 24: Compiling a C Assignment Using Registers.
Consider f = (g + h) - (i + j);
The variables f, g, h, i, and j are assigned to the registers $s0, $s1, $s2, $s3, and $s4, respectively. What is the compiled MIPS code?
Solution:
  add $t0, $s1, $s2 # register $t0 contains g + h
  add $t1, $s3, $s4 # register $t1 contains i + j
  sub $s0, $t0, $t1 # f gets $t0 - $t1, which is (g + h) - (i + j)

## Slide 25: Memory operands
Programming languages have simple variables that contain single data elements. They also have more complex data structures—arrays and structures. How can a computer represent and access such large structures?
The processor can keep only a small amount of data in registers, but computer memory contains billions of data elements. Hence, data structures (arrays and structures) are kept in memory.
Arithmetic operations occur only on registers in MIPS instructions; thus, MIPS must include instructions that transfer data between memory and registers. This is data transfer instructions

## Slide 26
To access a word in memory, the instruction must supply the memory address. Memory is just a large, single-dimensional array, with the address acting as the index to that array, starting at 0.
The data transfer instruction that copies data from memory to a register is traditionally called load.
The format of the load instruction is the name of the operation followed by the register to be loaded, then a constant and register used to access memory.
The actual MIPS name for this instruction is lw, standing for load word.
The format of the load instruction is the name of the operation followed by the register to be loaded, then a constant and register used to access memory

## Slide 27: Load word instruction.
g = h + A[8];

## Slide 28: Load word instruction.
Assume $s3 has 5000, and words addressed 5000..5002 have the data shown: 5000: 99 5001: 77 5002: 323
What address will be computed by: lw $t0, 2($s3)
2($s3) computes the address as 2 + (the value in $s3), so 2 + 5000, or 5002.

## Slide 29: Load word instruction.
Assume $s3 has 5000, and words addressed 5000..5002 have the data shown: 5000: 99 5001: 77 5002: 323
What value will be put in $t0 by: lw $t0, 0($s3)
0($s3) will compute the address 0 + 5000, or 5000. The value in the word at address 5000 is 99. Thus, 99 will be put in $t0.

## Slide 30: Load word instruction.
Assume $s3 has 5000, and words addressed 5000..5002 have the data shown: 5000: 99 5001: 77 5002: 323
What value will be put in $t1 by: lw $t1, 2($s3)
2($s3) will compute the address 2 + 5000, or 5002. The value in the word at address 5002 is 323. Thus, 323 will be put in $t1.

## Slide 31: Store word
Load word and store word are the instructions that copy words between memory and registers in the MIPS architecture.
Store copies data from a register to memory
The actual MIPS name is sw, standing for store word.

## Slide 32: Example of compiling using load and store.

## Slide 33
If $s3 has 900, what address does this instruction compute? sw $t0, 20($s3)
20($s3) computes 20 + (the value in $s3), so 20 + 900, or 920.

## Slide 34: Constant or immediate operands
Many times a program will use a constant in an operation
add immediate or addi.
addi $s3, $s3, 4 # $s3 = $s3 + 4

## Slide 35: Readings
Hennessy and Patterson 2.1 to 2.6