## Slide 1: Boolean Algebra, Gates and Digital Logic

## Slide 2: BOOLEAN ALGEBRA
Boolean algebra is an algebra for the manipulation of objects that can take on only two values, typically true and false, although it can be any pair of values.
Computers are built as collections of switches that are either “on” or “off,” Boolean algebra is a very natural way to represent digital information.
Digital circuits in digital electronics use low and high voltages, but for our level of understanding, 0 and 1 will suffice.
Boolean algebra is an algebraic structure defined on a set of elements B, together with two binary operators(+, .)

## Slide 3: Boolean Expressions
Boolean Algebra has operations we can be performed on binary objects or variables. When we combine the variables and operators form a Boolean expression
In Boolean algebra, all the variables have the values 0 or 1 and, in typical formulations, there are three operators
Three most common Boolean operators: AND, OR, NOT

## Slide 4: Boolean Expressions
The OR operator is written as , as in x+y. The result of an OR operator is 1 if either of the variables is 1. The OR operation is also called a logical sum, since its result is 1 if either operand is 1.
The AND operator is written as , as in xy. The result of an AND operator is 1 only if both inputs are 1. Th e AND operator is also called logical product, since its result is 1 only if both operands are 1.
The unary operator NOT is written as x’. Th e result of a NOT operator is 1 only if the input is 0. Applying the operator NOT to a logical value results in an inversion or negation of the value (i.e., if the input is 0 the output is 1, and vice versa).

## Slide 5: Boolean Identities
There are several laws of Boolean algebra that are helpful in manipulating logic equations

## Slide 6: Boolean Identities
De Morgan's Theorem
  (A + B)’ = A’B’
  (AB)’ = A’ + B’

## Slide 7: Truth Table for AND
Inputs | Outputs
x y | xy
0 0 | 0
0 1 | 0
1 0 | 0
1 1 | 1
The logical operator AND is typically represented by either a dot or no symbol at all. For example, the Boolean expression xy is equivalent to the expression x · y and is read “x and y.” The expression xy is often referred to as a Boolean product.
The result of the expression xy is 1 only when both inputs are 1, and 0 otherwise.
Inputs | Outputs
x y | xy
0 0 | 0
0 1 | 0
1 0 | 0
1 1 | 1

## Slide 8: Truth Table for OR
Inputs | Outputs
x y | x + y
0 0 | 0
0 1 | 1
1 0 | 1
1 1 | 1

## Slide 9: The Truth Table for NOT
Inputs | Outputs
x | y
0 | 1
1 | 0

## Slide 10: Gates and Digital Logic Circuits
The electronics inside a modern computer are digital.
Digital electronics operate with only two voltage levels of interest: a high voltage and a low voltage. All other voltage values are temporary and occur while transitioning between the values.
The fact that computers are digital is also a key reason they use binary numbers, since a binary system matches the underlying abstraction inherent in the electronics.
Rather than refer to the voltage levels, we talk about signals that are (logically) true, or 1, or are asserted; or signals that are (logically) false, or 0, or are deasserted.
The values 0 and 1 are called complements or inverses of one another.

## Slide 11: Digital Logic Circuits
Electronic circuits that handle information encoded in binary form (deal with signals that have only two values, 0 and 1)

## Slide 12: Gates Continued…
Asserted signal: A signal that is (logically) true, or 1.
Deasserted signal: A signal that is (logically) false, or 0.
Logic blocks are categorized as one of two types
  Combinational logic: A logic system whose blocks do not contain memory and hence compute the same output given the same input.
  Sequential logic: A group of logic elements that contain memory and hence whose value depends on the input as well as the current contents of the memory.

## Slide 13: Gates Continued
A gate is a device that implements basic logic functions, such as AND or OR.
An AND gate implements the AND function, and an OR gate implements the OR function.
Both AND and OR are commutative and associative, an AND or an OR gate can have multiple inputs, with the output equal to the AND or OR of all the inputs.
Th e logical function NOT is implemented with an inverter that always has a single input.
To draw a NOT, the common practice is to add “bubbles” to the inputs or outputs of a gate to cause the logic value on that input line or output line to be inverted.

## Slide 14: Symbols for AND gate, OR gate, and NOT gate(inverter), shown from left to right

## Slide 15: Three categories of gates
Basic gates: The basic gates are AND, OR & NOT gates.
Universal gates: NAND & NOR gates are called as universal gates.
Special gates: Ex-OR & Ex-NOR gates are called as special gates

## Slide 16: AND Gate Symbol and AND GATE Truth Table
A.B
The output of AND gate will be ‘1’, when all the inputs are ‘1’.

## Slide 17: OR Gate
A + B
The output of an OR gate will be ‘1’, when at least one of those inputs is ‘1’.

## Slide 18: NOT Gate
A NOT gate is a digital circuit that has single input and single output. The output of NOT gate is the logical inversion of input. Hence, the NOT gate is also called as inverter.
This NOT gate produces an output YY, which is the complement of input, A.

## Slide 19: Universal gates
NAND & NOR gates are called as universal gates. Because we can implement any Boolean function, which is in sum of products form by using NAND gates alone. We can also implement a Boolean function that is a product of sums form using NOR gate alone.
Any logical function can be constructed using AND gates, OR gates, and inversion
NOR gate: An inverted OR gate.
NAND gate: An inverted AND gate.

## Slide 20: NAND Gate
NAND gate is a digital circuit that has two or more inputs and produces an output that is the inversion of logical AND of all those inputs
Symbol for NAND
NAND gate operation is same as that of AND gate followed by an inverter
The truth table for the NAND-gate is like the one for the and-gate, except that all output values have been inverted:

## Slide 21: NOR gate
NOR gate is a digital circuit that has two or more inputs and produces an output that is the inversion of logical OR of all those inputs.
Symbol of NOR gate
The truth table for the nor-gate is like the one for the or-gate, except that all output values have been inverted:

## Slide 22: Summary

## Slide 23: Three Input AND Gate
A | B | C | A.B.C
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 24: Making A Three Input Gate

## Slide 25: In class Activity- Four Input AND Gate
Create a multiple input AND gate by drawing four input AND gate and its truth table

## Slide 26: In-class Activity
Create a multiple input OR gates by drawing three and four input OR gates and their truth tables

## Slide 27: Gates and Integrated Circuits
Gates are not sold individually
They are sold in units called integrated circuits (ICs).
A chip is a small electronic device consisting of the necessary electronic components (transistors, resistors, and capacitors) to implement various gates.

## Slide 28: Reading
Hennessy and Patterson Chapter 8.2 (Appendix B)